## Slide 1: EE4214 Project Demo
Vishesh Dewan
Lee Ying Cong

## Slide 2: Processor 1
Bar thread
Handles cursor updates if buttons are pressed > 250 ms
Updates bar display if outdated, then sleep(40)
Brick thread
Always in receiving block mode: takes info from messages and updates specific brick column display
Note: Bar uses a global variable
Bcol1/Bcol2 threads
Generates column numbers indicative of which columns should turn red -------------> sends message
Input
sem_wait()-> waits for sem_post signal from game thread
Reverts column(s) back to original colour  Sends message
Game thread
Blocking mailbox receive state, receives info from ball thread
Displays ball and other display boxes (speed, bricks left, etc.)
Updates score and resolves brick collision case conditional sem_post ->Sends message to brick display & ball thread
Mailbox receive
Mailbox send

## Slide 3: Processor 2
Ball thread
Does collision detection and determines ball’s coordinates
Does a blocking mailbox receive, extracts info about bar position , etc.
Sends message to game thread via mailbox containing info about coordinates, speed, etc.
Mailbox receive
Mailbox send
Sleep (time varies to ensure FPS)
MAILBOX MESSAGES
typedef struct {
int message_for;
int ballx;
int bally;
int brickrow;
int brickcol;
int speed;
} msg_ball;
typedef struct {
int message_for;
int bar_position;
int score;
int game_status;
int poweruphold;
int poweruplengthen;
int ballheldx;
} msg_game;
MESSAGE QUEUE
typedef struct {
int id;
int status;
int isRed;
} msg_col;

## Slide 4: Implementation details
-> mutexes (protect resources shared by threads, in case of lengthy calculations shared resource is copied into variable local to thread to keep mutex blocking short)
-> semaphore implementation
-> INCREMENT = SPEED* cos(angle of line of direction)
loop INCREMENT times -> change xdir by one (ydir in special cases) ->
ydir= xdir*tan(angle of line of direction)
xcoordinate = angle_origin_y + xdir
ycoordinate = angle_origin_y - ydir
Check for collision
Check for corner conditions (N,S,W,E)
Check for side conditions
Check for remaining corner conditions
INCREMENT
SPEED
15

## Slide 5: Features - FPS
-> for ball thread:
ballthread_timestamp = xget_clock_ticks();
……………………..
ballthread_timestamp2 = xget_clock_ticks();
ballthread_timeinterval = ballthread_timestamp2 - ballthread_timestamp;
if (ballthread_timeinterval == 0)
sleep(40);
else if (ballthread_timeinterval==1)
sleep(30);
else if (ballthread_timeinterval == 2)
sleep(20);
else if (ballthread_timeinterval==3)
sleep(10);
else if (ballthread_timeinterval >=4)
//do nothing
-> game thread displays ball immediately after receiving coordinates

## Slide 6: Features - Extra
-> Synchronized PAUSE functionality
-> Synchronized RESET functionality (can be done from WIN, LOSE, PAUSE, or NORMAL game state)
-> bar lengthening power up
-> ball holding power up